LAB 1 STACK	SUYOG DHAKAL 075BCT092

Theory:

Stack:
A stack is an ordered collection of items into which new items may be inserted and from which items may be deleted at one end called the top of the stack. The first inserted element can be removed only at last and the last inserted element first. This condition of operation is known as Last-In-First-Out (LIFO).

#### Infix:
A infix expression is a single letter, or an operator, proceeded by one infix strinf and followed by another infix string.
(A + B) + (C – D)

Prefix:
A prefix expression is single letter, or an operator, followed by two prefix strings. Every prefix strings longer than a single variable contains an operator, first operand and second operand.
++AB - CD

Postfix:
A post-fix expression is a single letter or an operator, preceeded by two post-fix strings. Every post-fix string longer than a single variable contains first and second operands followed by an operator .
AB + CD -

1.algorithm for push and pop operation in stack

push operation

1.START
2. initialize top=-1
3.Read element to be pushed
4.push function
if top = MAX-SIZE -1
print stack overflow
else
++top
A[top] = x
5.END

pop operation

1.START
2.initialize top = -1
3.pop function
if top = -1
print stack underflow
else
top - -
5.END

2a. infix expression to post-fix expression

1.Start
2.Push “(“onto Stack, and add “)” to the end of X.
3.Scan X from left to right and repeat Step 4 to 7 for each element of X until the Stack is empty.
4.If an operand is encountered, add it to Y.
5.If a left parenthesis is encountered, push it onto Stack.
6.If an operator is encountered, then:
1. Repeatedly pop from Stack and add to Y each operator (on the top of Stack) which has the same precedence as or higher precedence than operator.
2. Add operator to Stack.
   [End of If]
7.If a right parenthesis is encountered ,then:
1. Repeatedly pop from Stack and add to Y each operator (on the top of Stack) until a left parenthesis is encountered.
2. Remove the left Parenthesis.
   [End of If]
   [End of step 3 loop]
8.END.
2b.infix expression to prefix
1.Start
2.Push ‘)’ onto Stack, and add ‘(‘ to the end of X.
3.Scan X from right to left and repeat Step 4 to 7 for each element of X until the Stack is empty.
4.If an operand is encountered, add it to Y.
5.If a right parenthesis is encountered, push it onto Stack.
6.If an operator is encountered, then:
1. Repeatedly pop from Stack and add to Y each operator (on the top of Stack) which has the same precedence as or higher precedence than operator.
2. Add operator to Stack.
   [End of If]
7.If a left parenthesis is encountered ,then:
1. Repeatedly pop from Stack and add to Y each operator (on the top of Stack) until a right parenthesis is encountered.
2. Remove the left Parenthesis.
   [End of If]
   [End of step 3 loop]
8.END.

3. Evaluate the post-fix expression.

1. Start
2. EvaluatePostfix(exp)
{ create stack
for i=0 to length(exp)-1
{
    if(exp[i] is operand
push(exp[i])
    else if(exp[i] is operator)
{ pop(operand2)
 pop(operand1)
 result perform(exp[i],operand1,operand2)
 push(result)
}
}
   return top of stack
 }
3.END

4.paired parenthesis in mathematical expression

1.Start
2. checkPairedParenthesis(exp){
n= length(exp)
create stack s
for I=0 to n-1
{
if exp[i] is ‘(‘ or ‘{‘ or ‘[‘
push(exp[i])
elseif exp[i] is’)’ or ‘}’ or ‘]’
{	if( s is empty) or (top does not pair with exp[i])
return false
else
pop()
 }

}
return s is empty ? True : false

}

3.END

Conclusion and Discussion:

In this lab, we implemented stack operation using C++.
we implemented push pop operation in stack, evaluated post-fix operation, converted infix to prefix and post-fix, and developed the program for checking the parenthesis, whether it is balanced or not.